Processing OPEC data:
1. Raw Data

High-Frequency Files:
1. Copy from CF card → laptop → data computer
2. Convert from card format (binary) to ASCII format using PC9000 > File > Convert Data Files
3. Process data using EdiRe – see documentation on EdiRe for more information on how to use this.
  - loads high-freq data files and outputs 30 min averaged fluxes
4. Put outputted files in an appropriately named folder in /Matlab/Data/OPEC/EdiRe/<site>/Ouput/Fluxes/____
5. Organize data with Load_EdiRe_output.m
  - loads from path listed above
  - saves fluxes in a running file (stacked values for all years (2002—2010...) located in
    /Matlab/Data/Flux/OPEC/EdiRe/<site name>/Processed/<site>_EdiRe_all.mat
Clean EdiRe data using EdiRe_clean_all.m
- loads from output path listed in (5)
- uses thresholds set in /Matlab/Data/Flux/OPEC/EdiRe/Docs/<site>_EdiRe_OPEC_thresholds.csv
- A) cleans data, and saves to /Matlab/Data/Flux/OPEC/EdiRe/<site name>/Processed/<site>_EdiRe_all_cleaned.mat
- B) loads met data; finds timeshifts between flux and met data; shifts the flux data so that it conforms to the met data (for better or worse, this is better than shifting only some portions of met data to fit the OPEC data)
- C) Calculates CO2 storage using CO2 concentration from EC system and any intermediate height CO2 measurements (if applicable).
- advanced spike-removal and cleaning of fluxes (NEE, Hs, LE, etc)
- applies wind filtering (if applicable)
- saves final output to /Matlab/Data/Flux/OPEC/EdiRe/<site name>/Processed/<site>_EdiRe_flux.mat

10-minute averaged files:
1. Copy from CF card
2. May have to convert to ASCII format – PC9000 > File > Convert Data Files
3. Put data files in /Matlab/Data/Flux/OPEC/Raw1/<site>/DAT_all/
4. run OPEC_data_conditioner.m to ensure all data files have appropriate characters in them
  - loads from /DAT_all/ (with .dat extension)
  - saves to /DAT_all_L1/ (with .datL1 extension)
5. Organize with OPEC_process_all.m
  - loads from /DAT_all_L1/
  - calls OPEC_load_all.m to load and sort data
  - saves output to /Matlab/Data/Flux/OPEC/Organized2/<site>/<site>_10min_all.mat
6. Clean 10-minute data using OPEC_clean_all
  - loads from output directory given in (5)
  - uses thresholds set in /Matlab/Data/Flux/OPEC/Docs/<site>_OPEC_thresholds.csv
- A) cleans data, and saves to /Matlab/Data/Flux/OPEC/Cleaned3/<site>/<site>_10min_L2.mat
-B) Performs rotation correction for fluxes
- C) loads met data; finds timeshifts between flux and met data; shifts the flux data so that it conforms to the met data (for better or worse, this is better than shifting only some portions of met data to fit the OPEC data)
- D) Calculates CO2 storage using CO2 concentration from EC system and any intermediate height CO2 measurements (if applicable).
- advanced spike-removal and cleaning of fluxes (NEE, Hs, LE, etc)
- applies wind filtering (if applicable)
- saves final output to /Matlab/Data/Flux/OPEC/<site>_OPEC_flux.mat

Combining hhour data from both 10-minute and EdiRe sources:

1. Run OPEC_compare_methods.m
  - loads the original met data for each site (from the master in /Matlab/Data/Flux_Analysis/rEC/<site>.mat)
  - makes all the desired met data a continuous (2002—2010..) file
  - loads the original flux data (coming from Natalia and Josh), and timeshifts this data to conform with met data (this aligning all 3 types of flux data with met data.
  - saves the shifted original data to /Matlab/Data/Flux/OPEC/<site>_orig_flux.mat
  - looks at some differences between different processing methods – not important though
  *** This is where you should load in more met data into the master file (if desired)
2. Run OPEC_compare_flux_windows.m
  - Loads all 3 sources of flux data and reconciles them – uses EdiRe data first, followed by 10-minute data, followed by the original data – the reason this is necessary is because some HF and 10-min files have been lost/corrupted, so each method does not cover exactly the same time periods. We view EdiRe to be most reliable, as it has the most corrections:
  – EdiRe has WPL, Spectral, Rotation, Wind Direction
  – 10-minute has; WPL, Rotation, Wind Direction
  – Orig data has: WPL, Wind Direction
  - records the % of data that comes from each source
  - Plots data from all 3 OPEC sites on top of each other – allows for visual inspection of data that may have been processed for the wrong site (it happens)
  - Saves all the data (flux + met) in /Matlab/Data/Flux/OPEC/<site>_master.mat